## Slide 1: Underwater Source Separation Using Multi-Stage Independent Component Analysis in Semi-Anechoic Water Tank
Ridhwan Juniarga Pribadi, Wiratno Argo Asmoro.
Wirawan, Dhany Arifianto, Endang Widjiati, Mifta Nur Farid
Regional Conference of Acoustic and Vibraton 2017
Bali - November 2017

## Slide 2: Background
Suraj Kamal and Supriya M.H, 2011.“Blind Source Separation of Nonlinearly Mixed Ocean Acoustic Signals Using Slow Feature Analysis”

## Slide 3
Imagine when we have to put the sensor in different condition
Then we will have….

## Slide 4: Background
Suraj Kamal and Supriya M.H, 2011.“Blind Source Separation of Nonlinearly Mixed Ocean Acoustic Signals Using Slow Feature Analysis”
Different salinity
Different temperature
Different sound speed
multi channel propagation profile

## Slide 5: Background
Capturing small portion, to make lab scale experiment
Water tank was covered with absorber to avoid the reflection of sound wave
The salinity and water temperature can be controlled

## Slide 6
Then, how do we separate this mixed sound from different sources?

## Slide 7: Blind Source Separation / Independent Component Analysis (ICA)
Simplification of separation model
Blindly decomposing mixed sound without any prior information of the sources
Linear mixture model

## Slide 8: Assumption of ICA
Signals must be statistically independent
.......................(1)
Signal must be non-Gaussian

## Slide 9: Time Domain ICA (TDICA)

## Slide 10: Frequency Domain ICA (FDICA)

## Slide 11: MuItistage ICA (MSICA)

## Slide 12
So now our black box is complete
Experiment were performed in underwater tank
3 different methods of ICA were applied to estimate source signals

## Slide 13: Experiment setup
Side view
Top view
sensors
sources
sources
sensors

## Slide 14: Configuration of Test Signal
No | Signal | Note
1 | Puretone 500hz | Narrow Band
2 | Puretone 600hz | Narrow Band
3 | Puretone 700hz | Narrow Band
4 | Puretone 800hz | Narrow Band
5 | Puretone 900hz | Narrow Band
6 | Puretone 1 khz | Narrow Band
7 | Ship noise | Wideband Stationary
8 | Sonar Pinging | Wideband Non-Stationary

## Slide 15
How was the result then?

## Slide 16: Result of TDICA
Chart: MSE
| ping | 900hz | 900hz | 1000hz | 900hz | 1000hz | ship | ping | ship | 900hz | 600hz | 500hz
Distance 85 cm | 0.018745 | 0.088607 | 0.070964 | 0.079384 | 0.080907 | 0.063167
Distance 100 cm | 0.062883 | 0.11784 | 0.16639 | 0.21545 | 0.2134 | 0.19149
Distance 150 cm | 0.080466 | 0.15689 | 0.17153 | 0.19532 | 0.1843 | 0.27485

## Slide 17: Result of source separation (time-freq representation)
Each signal not decomposed perfectly
Intensity of signal 2 increased in this part

## Slide 18: Result of FDICA
Chart: MSE
| ping | 900hz | 900hz | 1000hz | 900hz | 1000hz | ship | ping | ship | 900hz | 600hz | 500hz
Distance 85 cm | 0.022396 | 0.058885 | 0.065418 | 0.075179 | 0.075995 | 0.075595
Distance 100 cm | 0.024071 | 0.075372 | 0.061949 | 0.078398 | 0.070993 | 0.062875
Distance 150 cm | 0.023689 | 0.066562 | 0.071525 | 0.074771 | 0.073086 | 0.073083

## Slide 19: Result of MSICA
Chart: MSE
| ping | 900hz | 900hz | 1000hz | 900hz | 1000hz | ship | ping | ship | 900hz | 600hz | 500hz
Distance 85 cm | 0.022953 | 0.0591 | 0.065474 | 0.076 | 0.082252 | 0.074154
Distance 100 cm | 0.024189 | 0.070029 | 0.06227 | 0.078143 | 0.073188 | 0.06591
Distance 150 cm | 0.027529 | 0.066099 | 0.069068 | 0.074997 | 0.081565 | 0.072431

## Slide 20: Comparison of 3 methods
Chart: Distance of Hydrophones and Sources
| 85cm | 100cm | 150cm
TDICA | 0.066962 | 0.16124 | 0.17723
FDICA | 0.062245 | 0.062276 | 0.063786
MSICA | 0.063322 | 0.062288 | 0.065281
Performance of TDICA decaying as distance of sources-sensors increased

## Slide 21: Distribution of testing signal
Distribution of Testing Signal Ship dan Ping ; (a) baseline ; (b) distance 85 cm; (c) dnstance 100 cm; (d) distance 150 cm

## Slide 22: Conclusion
MSICA and FDICA shows almost equal value of MSE, and the TDICA method shows significant decreasing of performance for each addition of recorded distance.
The signals still not well-reconstructed.
There was some reflected sound in water tank captured by sensors

## Slide 23: Kurtosis test signal
Chart: kurtosis
| pure500 | pure600 | pure700 | pure800 | pure900 | pure1000 | ship | ping
 | 1.9677 | 3.5008 | 2.7206 | 2.161 | 2.1551 | 1.5005 | 6.4091 | 5.9051
gaussian

## Slide 24: Covariance of test signal
sinyal | 1000Hz | 500Hz | 600Hz | 700Hz | 800Hz | 900Hz | ping | ship
1000Hz |  | -0.011 | 0.0007 | -4E-05 | 6E-05 | -6E-05 | -7E-04 | 3E-05
500Hz | -0.011 |  | 0.0027 | 0.001 | 5E-05 | 0.0003 | 0.0003 | -1E-04
600Hz | 0.0007 | 0.003 |  | -0.003 | 1E-05 | 0.0174 | -6E-05 | 3E-05
700Hz | -4E-05 | 0.001 | -0.003 |  | -2E-05 | -5E-05 | 7E-05 | -5E-06
800Hz | 6E-05 | 5E-05 | 1E-05 | -2E-05 |  | -2E-04 | 1E-05 | 0.0002
900Hz | -6E-05 | 3E-04 | 0.0174 | -5E-05 | -0.0002 |  | -1E-04 | -5E-05
ping | -7E-04 | 3E-04 | -6E-05 | 7E-05 | 1E-05 | -1E-04 |  | -6E-05
ship | 3E-05 | -1E-04 | 3E-05 | -5E-06 | 0.0002 | -5E-05 | -6E-05 | 

## Slide 25
underwater acoustic
Signal
Processing (BSS)
Yuwono, niken
Mencari nilai redaman dan kecepatan suara di akuarium objek
Belouchrani Amin
Memperkenalkan TFICA
Ridasari Fatma,
Menggunakan TFICA untuk memisahkan suara pompa tercampur
Wahyu Indra
Memisahkan sinyal tercampur sintetsis bawah air
TUGAS AKHIR
SAYA
Pratiwi Indan,
Melakukan uji waktu dengung di akuarium objek
1998
2011
2012
2012
2013
2013

## Slide 26: Simulasi Pencampuran Suara
Mixed signal
Mixing matrix
source signal
A. Belouchrani and M. G. Amin, 1998“Blind Source Separation Based on Time-Frequency Signal Representations”

## Slide 27: Preprocessing
centering
Whitening(sphering)

## Slide 28: Preprocessing
http://www.cs.bham.ac.uk/~axk/ML_ICA.ppt [diaksesFebruari, 2013]

## Slide 29: Mixture
LINEAR MIXTURE
CONVOLUTIVE MIXTURE